## Slide 1
RADIO FREQUENCY REMOTE CONTROL
A SEMINAR PROJECT PRESENTED BY
NWANZE FRANKLIN CHUKA
2011364033

## Slide 2: INTRODUCTION
Radio Frequency Remote control operates by transmitting radio frequency signals from one point to another.
The signals transmitted are in digital form and as such can be manipulated.

## Slide 3: BASIC COMPONENTS OF RF REMOTE CONTROL
TLP (TRANSMITTER MODULE) 433 AND RLP 433 (RECEIVER MODULE).
MICRO CONTROLLER

## Slide 4
MICRO CONTROLLER PIC 16F877A

## Slide 5: RF MODULE SPECIFICATIONS
Technical parameters of the receiver head
Operating voltage : DC5V
Receiving frequency: 433.92MHZ
Receiver sensitivity: - 105DB
Size : 30 * 14 * 7mm
external antenna: 32CM single core wire wound into a spiral
Technical parameters of the transmitter head
Launch distance: 20 -200 meters (different voltage, different results)
Operating voltage: 3.5-12V
Ways of working: AM
transfer rate: 4KB / S
transmit power: 10mW
Transmitting frequency: 433MHZ
Pin out from left → right: ( DATA ; VCC ; GND )

## Slide 6: BLOCK DIAGRAM OF RF REMOTE CONTROL
POWER SUPPLY
CONTROLLED DEVICE
TX
RX
MICRO CONTROLLER
MICRO CONTROLLER
KEYPAD
5V
12V
5V
5V
RF SIGNALS
ANTENNA

## Slide 7: FUNCTION OF MICRO CONTROLLER IN THE CIRCUIT
The micro controller performs the following functions
Encoding and Decoding
Noise Filtering
Transmitter and Receiver Synchronization
Redundancy check
Action initiation

## Slide 8: ENCODING TECHNIQUE (MANCHESTER)
This is a type of Non Return to Zero (NRZ) encoding technique where there is a transition from either HIGH to LOW or LOW to HIGH of every bit.

## Slide 9: WHY USE MANCHESTER ENCODING?
On idle state, the receiver module picks up stray radio frequency signals and if care is not taken it can be interpreted as‘1’ or ‘0’.
We use Manchester encoding technique in remote control to help the microcontroller detect when the transmitter is transmitting a long stream of zeros or ones

## Slide 10: MANCHESTER ENCODING ILLUSTRATED
1
1
1
0
0
0
0
1
0
0
1
1
0
0
1
0
1
1
0
0
1
Diagrammatic representation of bits
Diagrammatic representation of Manchester encoded bits